## Slide 1: Contents
ATM fundamentals
IP over ATM
ATM Local Area Networks
Advanced Network Technologies
Edited by: Szilveszter Kovács
e-mail: szkszilv@gold.uni-miskolc.hu

## Slide 2: ATM Fundamentals
Introduction
ATM Fundamentals
The ATM Signaling
The ATM Virtual Path and Virtual Channel
The ATM Cell Header Format
The ATM Reference Model
ATM Traffic Parameters and Transfer Capabilities
ATM Addressing
ATM Trunking and Routing

## Slide 3
Transfer mode
  a specific way of transmitting and switching information in a network
Synchronous transfer mode (STM)
  a data unit associated with a given channel is identified by its position (TDM)
  predefined channel bit rates (n*64kbs, E1: 2.048Mbps)
  end to end synchronous circuit
Channel
n
Channel
2
Channel
n
Channel
2
Framing signal
Periodic frame
Channel
1
Framing signal
Channel
1
Framing signal

## Slide 4
Asynchronous Transfer Mode (ATM)
  a data unit associated with a specific virtual channel may occur in any position
  flexibility of bit bit rate allocation ! (e.g. bandwidth allocation on demand)
  some problems:
    impacts of possible cell loss
    cell transfer delay
    cell delay variation
Quality
of
Service
Header
Cell
Channel
1
Header
Channel 3
Header
Channel
3
Header
Channel
unused
Header
Channel
1
Header
Channel
7

## Slide 5: ATM - fundamentals
Small fixed-size cells (5+48 byte, header+payload)
  too long  higher delays
  too short  too many overhead
ATM Cell Format :
Header
Payload
5
48
53 bytes
Connection oriented - cell switching
  low overhead  low processing time and delay
Cells
Cells
Virtual Channel

## Slide 6
Flexible, application independent (conversion of application data units to/from cells), it can handle
  low or high bit rate connection or
  dynamic bandwidth allocation

Voice
Video
Data
ATM Cells
Both LAN and WAN technology
  20 bytes structured hierarchical address format

## Slide 7: The ATM signaling
Signaling is used for managing connections
  user to network signaling (UNI User to Network Interface)
  inter exchange signaling (NNI Network to Network Interface)
ATM
switch
ATM
switch
ATM
switch
ATM
switch
UNI
NNI
UNI
NNI

## Slide 8: Virtual Path and Virtual Channel
ATM is connection oriented
The links (Transmission Paths TP) between network elements are carrying a hierarchical structure of connections:
  Virtual Channel (VC) ‘A concept used to describe unidirectional transport of ATM cells associated by a common unique identifier’ - the Virtual Channel Identifier (VCI)
  Virtual Path (VP) ‘A concept used to describe unidirectional transport of cells belonging to virtual channels that are associated by a common identifier’ - the Virtual Path Identifier (VPI)
ATM Physical Connection
Transmission Path
(e.g. E3, OC–12)
Virtual Path (VPI)
Virtual Path (VPI)
Virtual Channels (VCI)
Virtual Channels (VCI)
- Connections are identified by the VPI/VCI

## Slide 9
A connection could have different VPI/VCI identifier on each Transmission Path
VPI 2
TP 1
TP 3
TP 2
VPI 1
VCI 1
VCI 2
VCI 1
VCI 2
VCI 3
VCI 1
VCI 2
VPI 1
VCI 1
VCI 8
VPI 1
VPI 2
VPI 9
VCI 1
VCI 2
VCI 3
VCI 1
VCI 8
VPI 9
VPI 2
VPI 2
VPI 1
VP Switching
VC Switching
ATM
Switch

## Slide 10
ATM Switching Table
1/1
1:
1/2
1:
VPI/VCI
Port
TP
2/1
9/8
3:
2:
VPI/VCI
Port
TP
2/1
1:
2/2
1:
1/1
1/2
3:
3:
2/3
1:
1/3
3:
ATM
switch
1/1
TP1
1/2
2/2
TP2
TP3
2/1
9/8
1/2

## Slide 11
A concatenation of VC links is called Virtual Channel Connection (VCC)
A concatenation of VP links is called Virtual Path Connection (VPC)
Virtual Channel Connection (VCC)
Virtual Path Connection (VPC)
VP Switch
VC Switch
VC Switch
NNI
NNI
VPI = 2 VCI = 5
VPI = 1 VCI = 1
VPI = 9 VCI = 5
VPI = 7 VCI = 3
UNI
UNI
ATM
switch
ATM
switch
ATM
switch
1/1
2/5
9/5
7/3
Not modified! Only the Path is switched.

## Slide 12: The ATM cell header format
Depending on the signalling used, there are two different header format
Header
Payload
5
48
53 bytes
UNI Header Format:
GFC
VPI
4
VPI
8
16
PT
3
CLP
1
HEC
8
40 bits
NNI Header Format:
VPI
VPI
12
16
PT
3
CLP
1
HEC
8
40 bits

## Slide 13
UNI Header Format:
GFC - generic flow controll, for identifying multiple stations sharing a single ATM interface (typically not used: GFC=0000)
VPI - virtual path identifier, conjunction with the VCI identifies the next destination of the cell passing through the ATM switch
VCI - virtual channel identifier
PT - payload type, 3 bits indicating: 1. bit: user data, or control, 2. bit: congestion, 3. bit: indicates, whether the cell is the last in a series of cells representing an AAL5 frame
CLP - congestion loss priority bit, indicates whether the cell should be discarded in case of congestion (CLP=0, dont discard)
HEC - header error control, checksum calculated only on the header
GFC
VPI
4
VPI
8
16
PT
3
CLP
1
HEC
8
40 bits
NNI Header Format:
VPI
VPI
12
16
PT
3
CLP
1
HEC
8
40 bits

## Slide 14: The ATM Reference Model
Physical layer
  transmission and receipt bits
  framing
    keeping tracks of cell boundaries
    packaging cells to frames
Physical layer
ATM layer
ATM adaptation layer
Higher layers
Higher layers

## Slide 15: The ATM Reference Model
ATM layer
  establishing connections and passing cells through ATM network
    cell header handling, inserting and removing
    cell relay
    multiplexing and demultiplexing connections
Physical layer
ATM layer
ATM adaptation layer
Higher layers
Higher layers

## Slide 16: The ATM Reference Model
ATM adaptation layer (AAL)
  adaption of services provided by the ATM layer to the requirements of the higher layer
    set-up/terminate end-end virtual channel
    segmentation/reassembly of messages to/from cells
    control Quality of Service delivery
    flow control
Physical layer
ATM layer
ATM adaptation layer
Higher layers
Higher layers
Physical
ATM
Physical
ATM
Physical
ATM
AAL
Application
Signaling
Management
Physical
ATM
AAL
Application
Signaling
Management

## Slide 17
Transmission Convergence sublayer
  Cell delineation - maintains ATM cell boundaries
  Header error control sequence generation and verification (8 bit CRC for the header only) - to ensure valid data
  Cell rate decoupling - inserts or suppresses idle (unassigned) ATM cells to adapt the rate of valid ATM cells to the payload capacity of the transmission system
  Transmission frame adaptation - packages ATM cells to frames acceptable to the particular physical layer implementation
  Transmission frame generation and recovery - generates and maintains the appropriate physical layer frame structure
Physical Media Dependent sublayer
Physical layer - two sublayers:
Physical layer
TC
PMD

## Slide 18
Physical Media Dependent sublayer
  responsible for sending and receiving continuous flows of bits with associated timing information to synchronize transmission and reception
  physical medium dependent: (includes only physical medium dependent functions)
ATM SDH/SONET bit rates
SDH—Synchronous Digital Hierarchy
SONET—Synchronous Optical Network
SDH
SONET
Mbps
STM-1
STM-4
STM-8
STM-16
STS-1/OC-1
STS-3/OC-3
STS-12/OC-12
STS-24/OC-24
STS-48/OC-48
51.84
155.52
622.08
1,244.16
2,488.32
CCITT (Consultative Committee for International Telephony and Telegraph)
ITU (International Telecommunications Union)
STM—Synchronous Transport Module
STS—Synchronous Transport Signal
OC—Optical Carrier

## Slide 19
ATM can use any physical medium capable for carrying ATM cells
Speed (Mbps)
DS1 E1 J2 DS3 E3 E4
1.544 2.048 6.23 45 34 139
Framing
Standardized physical mediums and max. distances
Multi- Mode Fiber
Single- Mode Fiber
Coaxial Cable
UTP–5
UTP–3
STP
ATM25 STS 1 STS3c/STM1
25.6 51.8 155
STS 12c/STM4 4B/5B (FDDI-TAXI) 8B/10B (Fiberchannel)
622 100 155
100m 2km exists
100m 100m 100m
100m 100m
100m
exists exists exists exists
exists exists
2km
15km+
15km+
exists
Plastic Fiber
50m
50m

## Slide 20: ATM layer
Establishing connections and passing cells through ATM network - ATM switching
Physical layer
ATM layer
VPI 2
TP 1
TP 3
TP 2
VPI 1
VCI 1
VCI 2
VCI 1
VCI 2
VCI 3
VCI 1
VCI 2
VPI 1
VCI 1
VCI 8
VPI 1
VPI 2
VPI 9
VCI 1
VCI 2
VCI 3
VCI 1
VCI 8
VPI 9
VPI 2
VPI 2
VPI 1
VP Switching
VC Switching
1/1
1:
1/2
1:
VPI/ VCI
Port
2/1
9/8
3:
2:
VPI/ VCI
Port
2/1
1:
2/2
1:
1/1
1/2
3:
3:
2/3
1:
1/3
3:
-
-
-
-
-

## Slide 21
Connection Types
Connection oriented - cell switching
  all the cells are travelling on the same path (virtual channel)
  it guarantees the cell sequence integrity (under normal fault-free conditions) (nowhere in the network can a cell belonging to a specific virtual channel connection overtake another cell of the same virtual channel connection that has been sent earlier)
  Point-to-point connection types
Point-to-multipoint connection types
Cells
Cells
Virtual Channel

## Slide 22
Point-to-point connection types
  unidirectional or bidirectional
Cells
Cells
Virtual Channel
Point-to-multipoint connection types
  unidirectional only
  bidirectional through additional point-to-point connections (multicast server)
multicast server

## Slide 23
Connection Services
Permanent Virtual Circuit (PVC)
7/2
ATM
switch
ATM
switch
ATM
switch
ATM
switch
B
9/2
1/1
A
D
C
9/5
2/3
9/5
1/5
9/3
1
2
3
4
1
2
1
2
1
2
3
4
1/5
1:
9/3
2:
VPI/ VCI
Port
2/3
7/2
3:
4:
VPI/ VCI
Port
-
-
7/2
1:
VPI/ VCI
Port
9/2
2:
VPI/ VCI
Port
-
2/3
1:
VPI/ VCI
Port
1/1
2:
VPI/ VCI
Port
-
9/2
1:
1/1
2:
VPI/ VCI
Port
9/5
9/5
3:
4:
VPI/ VCI
Port
-
-
VPI/VCI tables are handled manually, the connections are administratively established/released

## Slide 24
Switched Virtual Circuit (SVC)
VPI/VCI tables are automatically handled , the connections are established/released through (UNI/NNI) signaling procedure
ATM
switch
ATM
switch
ATM
switch
ATM
switch
B
1/1
A
D
C
9/5
2/3
1/5
1
2
3
4
1
2
1
2
1
2
3
4
1/5
1:
VPI/ VCI
Port
2/3
3:
VPI/ VCI
Port
-
VPI/ VCI
Port
VPI/ VCI
Port
1/1
2:
VPI/ VCI
Port
9/5
4:
VPI/ VCI
Port
-
NNI signaling
2/3
1:
VPI/ VCI
Port
1/1
2:
VPI/ VCI
Port
-
UNI signaling
UNI signaling

## Slide 25
Soft Permanent Virtual Circuit (Soft PVC)
  User - network connections are established/released administratively
  Network - network connections through NNI signaling procedure
ATM
switch
ATM
switch
ATM
switch
ATM
switch
B
1/1
A
D
C
9/5
2/3
1/5
1
2
3
4
1
2
1
2
1
2
3
4
1/5
1:
VPI/ VCI
Port
2/3
3:
VPI/ VCI
Port
-
VPI/ VCI
Port
VPI/ VCI
Port
1/1
2:
VPI/ VCI
Port
9/5
4:
VPI/ VCI
Port
-
NNI signaling
2/3
1:
VPI/ VCI
Port
1/1
2:
VPI/ VCI
Port
-
Handled manually
Handled manually
Handled by NNI signaling

## Slide 26
ATM adaptation layer (AAL)
Adaptation of services provided by the ATM layer to the requirements of the higher layer
AAL is subdivided into two sublayers
  convergence (CS) sublayer
    service dependent
    provides the AAL service at the AAL SAP (Service Access Point) for the higher layers
  segmentation and reassemby (SAR) sublayer
    segmentation/reassembly of higher level PDUs (Protocol Data Unit) to/from the information field of the ATM cells (48 byte)
AAL
CS
SAR
ATM layer
AAL
Higher layers

## Slide 27
Adaptation Layer Service Classes
To minimize the number of AAL protocols service classes are defined
Each service class need specific CS and SAR sublayer
There are different Adaptation Layer Types (AAL protocols) for serving the different service classes
Timing relation between source and destination
Bit rate
Connection mode
Class A
Class B
Class C
Class D
Not required
Required
Constant
Variable
Connection-oriented
Connectionless
Circuit emulation,
e.g. constant bit rate video
E.g. variable
(compressed)
bit rate video
Connection-
oriented
data transfer
Connectionless
data transfer

## Slide 28
Adaptation Layer Types
Each AAL type has different service class and specific CS and SAR sublayer
AAL type 1 (Class A)
  synchronous traffic with constant bit rates
    e.g. voice, or video
AAL type 2 (Class B)
  synchronous traffic with variable bit rates
    e.g. compressed video
AAL type 3/4 (Class C/D)
  datagram transport
AAL type 5 (Class C)
  datagram transport (simpler)

## Slide 29
AAL type 3/4
The AAL 3/4 Convergence Sublayer (CS) creates a Protocol Data Unit (CS PDU) from the data Frame
Frame (1 - 65 5353 byte)
CS PDU:
CPI
Btag
BAsize
PAD
AL
Etag
Length
CS PDU Payload
8
8
16
0..24
8
8
16 bit
CPI Common Part Indicator, version number
Btag/Etag Beginning/Ending Tag, help proper association of the CS PDU header and trailer (same numeric value is set both fields)
BAsize Buffer Allocation Size, indicates to the receiving peer entity the maximum buffering requirements to receive the CS PDU
PAD, ensures, that the payload must be an integer multiple of four bytes
AL Alignment, is used for 32 bit alignment of the CS PDU trailer
Length, the length of the CS PDU payload field (detects loss or gain)

## Slide 30
AAL type 3/4
The AAL 3/4 Segmentation and Reassemby (SAR) sublayer creates ATM cells (SAR PDU-s) from the CS PDU
ST Segment Type, first/middle/last cell, or single cell message
SN Sequence Number, mod 16 counter on the cell sequence
MID Multiplexing Identifier, identifying multiple PDU on a single VC
LI Length Indicator, the length of valid data (from the CS PDU) in the payload field in bytes
CRC, 10 bit CRC on SAR PDU header and payload (detects errors)
CS PDU
SAR PDU:
ATM Header
ST
SAR PDU Payload
5 byte
2 bit
SN
4 bit
MID
10 bit
LI
6 bit
44 byte
CRC
10 bit
SAR PDU Payload
44 byte
SAR PDU Payload
44 byte
SAR PDU Payload
44 byte
48 byte ATM cell payload

## Slide 31
AAL type 5
The goal is to reduce of the overhead of the AAL 3/4
Variable bit rate without timing relation between the source and the destination
AAL 5 is not supporting multiplexing (in spite of AAL 3/4)
The AAL 5 CS creates a CS PDU from the data Frame
Frame (1 - 65 5353 byte)
CS PDU:
PAD
UU
Length
CS PDU Payload
0..47 byte
8 bit
16 bit
PAD, 48 byte alignment of the CS PDU (ATM cell payload)
UU User-to-User identification, used for transparent transfer of CS user-to-user information
CPI Common Part Indicator, version number (same as in AAL 3/4)
Length, the length of the CS PDU payload field (detects loss or gain)
CRC, 32 bit CRC on CS PDU (detects errors)
CPI
8 bit
CRC
32 bit

## Slide 32
AAL type 5
The AAL 5 Segmentation and Reassemby (SAR) sublayer creates ATM cells (SAR PDU-s) from the CS PDU
ATM Header PT (Payload Type) field 3. bit: indicates, whether the cell is the last in a series of cells representing an AAL5 CS PDU
SAR PDU:
CS PDU
SAR PDU Payload
48 byte
SAR PDU Payload
48 byte
SAR PDU Payload
48 byte
ATM Header
SAR PDU Payload
5 byte
48 byte full ATM cell payload
1
ATM Header
SAR PDU Payload
0
ATM Header
SAR PDU Payload
0
The last one

## Slide 33
AAL type 3/4 ATM cell overhead
ATM Header
5 byte
SAR PDU Payload
44 byte
SAR PDU Header
2 byte
SAR PDU Trailer
2 byte
ATM cell payload (48 byte)
ATM Header
5 byte
SAR PDU Payload
48 byte
ATM cell payload (48 byte)
AAL type 5 ATM cell overhead

## Slide 34
ATM traffic parameters and transfer capabilities
To be able to optimize the ATM network operation, ATM traffic is grouped into various categories of connections with different traffic characteristics:
  source traffic descriptor - the source’s connection request:
    e.g. peak cell rate, average cell rate, cell delay variation tolerances, burstiness, peak duration
Based on the required traffic parameters (source traffic descriptor) and the network transfer capabilities - a ‘traffic contract’ can be established between the user and the network
The traffic contract is negotiated between the user and the network during the connection establishment (signaling)
Conformance to the negotiated traffic contract can be enforced by the network

## Slide 35
A set of source traffic parameters
Peak Cell Rate (PCR)
  the maximum cell rate at which a source may send its cells during the connection’s lifetime
Sustainable Cell Rate (SCR)
  always smaller than the PCR (an average cell rate)
  parameter used for burst-type traffic
Maximum Burst Size (MBS)
  the amount of cells which may be sent at the PCR
Minimum Cell Rate (SCR)
  the minimum cell rate which is guaranteed by the network for the source during the connection’s lifetime
ATM Source traffic descriptor

## Slide 36
Cell Loss Ratio
  ratio of lost cells to transmitted cells
Mean Cell Transfer Delay (MCTD)
  average of the cell delay between the endpoints
Cell Delay Variation Tolerance (CDVT)
  jitter, the maximal allowed variation of the cell transfer delay on the same connection
ATM performance parameters - the Quality of Service (QoS)

## Slide 37
Constant Bit Rate (CBR)
  used by connections requesting a fixed amount of bandwidth to be continuously available during the connection’s life time (e.g. real time video)
Variable Bit Rate (VBR) (real time / non real time)
  suitable for applications with varying bit rate requirements where there exists prior knowledge of some traffic characteristic (e.g. compressed real time video)
Available Bit Rate (ABR)
  supports LAN-like applications, where users accept unreserved bandwidth but want to make optimum use of the bandwidth actually available
Unspecified Bit Rate (UBR)
  the best effort service, but no guarantee on cell loss and delay (e.g. Internet)
ATM transfer capabilities - Service Classes
(According to the ATM Forum)

## Slide 38
ATM Service Classes and the Quality of Service
(According to the ATM Forum)
Constant Bit Rate
Cell Loss Ratio
Cell Transfer Delay
Cell Delay Variation
Peak Cell Rate
Sustainable Cell Rate Burst Tolerance
Minimum Cell Rate
Variable Bit Rate Real Time
Variable Bit Rate Non RT
Specified
Available Bit Rate
Unspecified Bit Rate
Specified
Specified
n/a
n/a
Specified
Specified
Specified
Unspecified
Unspecified
Specified
Specified
Specified
n/a
Mean CTD only
Specified
Specified
Un- specified
n/a
n/a
n/a
n/a
Specified
Specified
Specified
n/a : Not applicable

## Slide 39
Mechanisms to achive a specified QoS
Connection Admission Control (CAC)
  negotiation of the traffic contract is between the user and the network in the call establishment phase
Usage and Network Parameter Control (UPC, NPC)
  ‘Traffic Policing’ - a set of actions taken by the network to monitor and control that the traffic contract is respected in terms of traffic offered and validity of the ATM connection, at the user access and the network access respectively
Traffic Shaping
  altering the tarffic characteristics on the user side to ensure conformance to the traffic contract, e.g. reducing the peak cell rate by buffering

## Slide 40
negotiation of the traffic contract is between the user and the network in the call establishment phase
CAC is provided with:
  the required ATM layer transfer capability
  the source traffic descriptors
  the required QoS class
a connection can only be accepted if sufficient network resources are available to establish the connection end-to-end with is required quality of service
  e.g. for a required CBR service class the available link capacity needs to be checked; for a required UBR service class the available buffer space could be the primer factor to be considered
Connection Admission Control (CAC)
Network
Contract

## Slide 41
‘Traffic Policing’ - a set of actions taken by the network to monitor and control that the traffic contract is respected
Checking the validity of VPI/VCI values
Monitoring the traffic volume entering the network from all active VP and VC connections to ensure that the agreed parameters are not violated
In case of traffic contract violation UPC/NPC can
  discarding cells that violate the negotiated parameters
  the ‘guilty’ connection may be released
  tagging of violating cells and discard later if necessary (CLP - congestion loss priority bit in ATM header)
  do nothing (forwarding)
Usage and Network Parameter Control (UPC, NPC)
Network
Contract
?
UPC

## Slide 42
altering the traffic characteristics on the user side to ensure conformance to the traffic contract, e.g. reducing the peak cell rate by buffering - better network utilisation, but increased cell transfer delay
Traffic Shaping
ATM Network
Contract
PCR
PCR
Contract
UPC: OK
Traffic Shaping

## Slide 43
ATM Addressing
The ATM address identifies the ATM End-System (AES)
The ATM address may differ depending upon whether the end-system connects to private or public ATM network
Several ATM address formats have been developed, one for public networks, and two for private networks
For private networks, ATM Forum has defined the use of the Network Service Access Point (NSAP) address format (not a true NSAP address, it does not terminate at the Network Layer)
Public ATM networks are using the globally unique E.164 numbers (it is also used by the Narrowband Integrated Services Network (NISDN)) ( 8 byte - 16 digit ISDN telephone number ) (only the UNIs connected directly to the public network will be assigned E.164 addresses)

## Slide 44
All ATM NSAP addresses have the following format:
ATM Prefix (Initial Domain Part IDP)
13 byte
ESI
6 byte
Sel
1 byte
20 bytes
ESI : End-System Identifier, 6 byte, must be unique within a particular IDP (in almost all cases it is the globally unique IEEE 802 Media Access Control (MAC) Address)
SEL : Network Service Access Point (NSAP) Selector, used by ATM end-systems for multiplexing to identify subinterfaces (not used for routing)
The ATM End-System (AES) NSAP format

## Slide 45
AFI (39)
DCC ATM Address Format :
1
DCC
2
DFI
1
AA
3
Reserved
3
RD
2
Area
2
ESI
6
Sel
1 byte
20 bytes
AFI (47)
ICD ATM Address Format :
1
ICD
2
DFI
1
AA
3
Reserved
3
RD
2
Area
2
ESI
6
Sel
1 byte
20 bytes
AFI : Authority and Format Identifier
identifies the type of the address
DCC : Data Country Code (ISO 3166)
ICD : International Code Designator (British Standard Institute)
DFI : Domain specific part Format Identifier, identifies the format used by the body
AA : Administrative Authority an organisational identifier (structuring the reminder of the address)
RD : Routing Domain
Area : Area identifier
ESI : End System Identifier (MAC Address)
SEL : NSAP Selector
(to identify subinterfaces)

## Slide 46
The E.164 Address Format (Global ISDN numbering plan: 8 byte - 16 digit)
1.digit: Unicast, or Multicast address
2-4: Country code (1-3 digit)
3-16: Area, City, Exchange, End-System
(nationally assigned)
AFI (45)
NSAP encapsulated E.164 Address Format :
1
E.164 Address
8 byte
RD
2
Area
2
ESI
6
Sel
1 byte
20 bytes

## Slide 47
ATM
switch
VPI/VCI
0/16
Automatic ATM End-System address prefix configuration
ATM
End-System
Interim Local Management Interface (ILMI):
Peer-to-peer network management protocol (ILMI reserved VCC: VPI=0, VCI=16)
Each device participating in the ILMI implements the ATM Management Entity (AME)
ILMI uses SNMP message syntax (Simple Network Management Protocol) and ILMI MIB (Management Information Base)
ILMI MIB supports interface configuration, max. number of supported connections, speed, media type, operational status, etc., address registering
AME
AME
ESI = acdc.3124.efa8
ATM Prefix = ?
VPI/VCI
0/16
ATM Prefix =
47.0091.0000.0000...

## Slide 48
ATM Trunking and Routing
Interim Interswitch Signaling Protocol (IISP)
Standardised by the ATM Forum
IISP provides table based rerouting, but no topology discovery (intended as an interim solution for small ATM networks)
It is also called PNNI Phase 0
Private Network-Network Interface (PNNI)
Standardised by the ATM Forum
PNNI is both Signaling and Routing Protocol
PNNI is supporting topology discovery via the distribution of reachability information, hierarchical routing and addressing and QoS (applied on the majority of ATM networks)
It is also called PNNI Phase 1

## Slide 49
IP over ATM
IP over ATM Fundamentals
Encapsulation
Addressing and Routing
Address Resolution
Next Hop Resolution Protocol

## Slide 50
IP over ATM
Transmission Control Protocol and Internet Protocol (TCP/IP) are one of the most widely used protocol suites in the computer communication area
(The popular Internet and WWW are based on IP)
IP is a connectionless protocol. IP datagrams contain the source and destination address.
IP packets are transferred in a best-effort manner:
- no error correction capabilities
- no QoS guarantees
- no information about successful delivery
- the correct order of the datagram fragments is not guaranted

## Slide 51
Higher layers over IP
TCP - Transmission Control Protocol and Internet Protocol - connection-oriented reliable transport protocol
UDP - User Datagram Protocol
- connectionless unreliable transport protocol
Native ATM ABR (Available Bit Rate) and ATM UBR (Unspecified Bit Rate) transfer capabilities are developed for data connection and able to substitute TCP/IP
- they might be build the Internet of the future -
but at the moment (and in the near future) TCP/IP-based networks are essential in internetworking
IP over ATM

## Slide 52
This model considers ATM to be a ‘wire’ for the transport of higher-layer (similar to LANE, but instead MAC, it uses IP addresses)
The model describes the transmission of IP datagrams, their encapsulation into ATM cells and the ATM address resolution protocol (ATM-ARP)
The IP network is a logical association of network elements (hosts, routers), which is independent of the underlying ATM networks
Carrying IP traffic over ATM-based network
The most mature mechanism is based on RFC 1577 ‘Classical IP and ARP over ATM’ (Internet Engineering Task Force IETF, 1994, update in 1996):

## Slide 53
Logical IP Subnetwork (LIS):
A group of IP nodes (hosts or routers) that connected to a single ATM network and belonging to the same IP subnetwork
Connections towards an IP node outside the LIS must be conveyed via IP router (IP node connected to more LISs)
An ATM endpoint can belong to several LISs via a single physical interface
IP routers between LISs, could be easily become a bottleneck - Next Hop Resolution Protocol (NHRP) could solve this problem
Within a LIS all ATM connections are VCCs (permanent (PVC), or switched (SVC))
The IP Maximum Transfer Unit (MTU) sizes within a LIS are the same for all VCs (9180 bytes)

## Slide 54
Main questions to solve:
Encapsulation
Routing
Addressing/address resolution
Carrying IP traffic over ATM-based network

## Slide 55
In traditional LAN conventions ‘encapsulation’ denotes the Logical Link Control (LLC) layer multiplexing and addressing - higher layer protocols are encapsulated with the LLC information
This LLC information can be considered as being a ‘in-band’ signaling message which addresses the higher layer data packets to the destination
In ATM networks ‘out-of-band’ signaling is used (signaling information is conveyed via separate virtual connection and not bounded to the actual user data-transfer)
IP over ATM - a way of ‘marry’ the two world - many solutions exists
Encapsulation:

## Slide 56
The three main encapsulation schemes:
The greater the amount of the multiplexing and addressing function realised in the end-station, the less information needs to be transported via the ATM signaling protocol
ATM
AAL 5
LLC
IP
TCP
Higher
layers
ATM
AAL 5
IP
TCP
Higher
layers
ATM
AAL 5
TCP
Higher
layers
TULIP/ TUNIC:
VC multiplexing:
LLC/SNAP encapsulation:
LLC: Logical Link Control
SNAP:
Subnetwork Attachment Point
VC: Virtual Channel
TUNIC: TCP and UDP over non-existent IP
AAL:
ATM Adaption Layer (Type 5: simple datagram transport)

## Slide 57
LLC/SNAP encapsulation: ( Logical Link Control / Subnetwork Attachment Point )
ATM
AAL 5
LLC
IP
TCP
Higher
layers
This scheme identifies the protocol by an IEEE 802.2 LLC Type 1 (unacknowledged, connectionless mode) header, which is followed by a Subnetwork Attachment Point (SNAP) header
LLC (3 byte) 0xAA-AA-03
OUI 0x00-00-00
Ether type 0x08-00
LLC indicating the presence of SNAP header
SNAP header, 3+2 byte Oraganizationally Unique Identifier and the indication of Ethertype
IP Protocol Data Unit
Most of the multiplexing function needs to exist in the end-station (generating, evaluating the LLC/SNAP header), the LLC entity constitutes the endpoint for the ATM/AAL5 connection, no information about the sender’s higher layer protocol is transmitted via the ATM signaling channel
Best suited for PVC-based ATM networks, or networks not capable of carrying many parallel VCs (however, SVC connection is also defined RFC 1755), several higher-layer protocol can share a single VCC
IP PDU up to 216-9 byte

## Slide 58
Example:
TCP over ATM - LLC/SNAP encapsulation
LLC/SNAP header
TCP
IP
LLC/SNAP
AAL 5
ATM
PHY
TCP Packet
IP Datagram
Add 5 Byte headers with VPI/VCI and CLP
App Data
TCP header
IP header
App Data
TCP header
IP header
App Data
TCP header
Convergence Sublayer (CS)
SAR
Put in 48 Byte cells—SAR into PDU
Transmission Convergence (STS, STM, DS)
Physical Media (MMF, SMF, STP, UDP,…
LLC/SNAP header
App Data
TCP header
IP header
CS tax

## Slide 59
VC multiplexing:
This scheme is also known as ‘null encapsulation’ (the LLC function does not exists)
Layer 3 packets (such as IP) are directly mapped onto an ATM/AAL 5
The ATM signaling specifies the Layer 3 entity as the ATM destination for the connection
The VC multiplexing incurs less overhead than LLC/SNAP encapsulation it requires many VCCs, separate one for each individual Layer 3 protocol pair between two ATM endpoints (generating potentially high amounts of signaling traffic)
ATM
AAL 5
IP
TCP
Higher
layers

## Slide 60
TULIP / TUNIC :
Eliminates the entire IP network layer, ATM AAL 5 connection exists directly between transport layer entities (such as TCP, UDP)
Major restriction: it requires single hop reachability between endpoints (for lack of IP, there are no intermediate IP routers either)
Simple end-station multiplexing and addressing functions, high demand for the ATM signaling protocol
For the future networks at the moment: having single hop reachability and higher-layer protocols demand support for different QoS levels
ATM
AAL 5
TCP
Higher
layers
TULIP: TCP and UDP over Lightweight IP
TUNIC: TCP and UDP over a Non-existent IP Connection

## Slide 61
Summary :
Encapsulation method:
LLC/SNAP
VC multiplexing
TUNIC
Source address Destination address Protocol family Protocol Port
Demultiplexing in end-sytem:
in signaling message:
Source address Destination address Protocol Port
Protocol family
Nothing
Source address Destination address Protocol family Protocol Port
Nothing
Default method for ‘classical IP and ARP over ATM’, it provides simple and smooth internetworking with existing procedures; LANEv2, MPOA
For the future at the moment (QoS)
Application:
Less overhead; LANEv2
LLC/SNAP: TCP (connection oriented) - IP (connectionless) - ATM (connection oriented)

## Slide 62
Addressing and routing
Most commonly used addressing model
Both IP and ATM addresses are used
For IP  ATM address mapping the ARP/RARP mechanism is adopted
Overlay model
This model assumes, that the IP addresses (Network Layer Address)are algorithmically mapped into (NSAP-based) ATM addresses.
Routing information can be easily exchanged among IP hosts/routers and ATM network entities - while each network retains its classical routing mechanisms
No need for separate ARP mechanism
A connection set-up request containing an IP address could be routed directly by the routing mechanism of the ATM (e.g. PNNI)
Disadvantage: Using different routing protocols in the IP and ATM networks may lead to less optimal end-to-end routes
Peer model

## Slide 63
Based on PNNI (Private Network Network Interface)
Route calculations are taking account the network topologies and the link states of both the IP and ATM network
Optimal route for IP packets in mixed IP/ATM environments
Integrated model
Further extension of the integrated model
It uses the PNNI protocol for routing in ATM switches and router based IP networks (it is also called integrated PNNI)
Because of the PNNI it may lead to optimal end-to-end routes through switched and routed networks as well
It supports QoS routing - suites well for the integrated services Internet
Integrated routing model

## Slide 64
Address resolution (in Overlay model)
Classical IP over ATM mechanism is required to resolve target IP address to target ATM address and vice versa
ATM-ARP is based on the ‘normal’ ARP and inverse ARP
No direct broadcast capabilities of the ATM network - specific ATM-ARP server needs to be deployed
Each LIS needs at least one ATM-ARP server (all ATM-ARP stay within a LIS)
The ATM-ARP servers are found via configured unique ATM addresses
Host stations are periodically registering their IP and ATM-SNAP or E.164 addresses to their ATM-ARP server (belonging to the same LIS)
The registered addresses are stored in the server’s database (ageing)
ATM-ARP packets are LLC/SNAP encapsulated and transported via an ATM/AAL5 VCC

## Slide 65
Clients are sending ATM-ARP requests (IPATM) to the ATM-ARP server of the LIS, based on the ATM address returned, they can establish a VCC (SVC) to the desired destination
The SVCs established are not immediately released after communication, but prior to any subsequent data transmission the clients must revalidate their own address mapping (ATM-ARP request to the ATM-ARP server) - in case of no respond from the ATM-ARP server, an InvARP request can be sent directly to the destination client (via the still existing SVC). Having no replay either, the destination can no longer be reached via the existing connection and the SVC is released.
IPA host
ATM-ARP server
IP
ATM
IP
ATM
IPB
ATMB
IPB host
SVC
ARP
ATMB
ATMB
IPB
InvARP

## Slide 66
Next Hop Resolution Protocol (NHRP)
Classical IP and ARP over ATM: connections between hosts in different LISs are established via (several) router hops - every router constitutes a potential bottleneck
The Next Hop Resolution Protocol (NHRP) allows a cut-through connection through several LISs to be established (direct end-to-end transparent ATM connection - it allows e.g. the ATM’s QoS capabilities to be exploited)
The Next Hop Server (NHS) performs the NHRP and realises the inter-LIS ARP mechanism (mapping ATM addresses to IP addresses outside the LIS)
If the destination host is not part of the ATM network, NHS provides the address of the egress router through which this destination can best be reached
NHRP is used for MPOA (Multiple Protocol Over ATM) also (it could be adopted for classical IP networks on broadcast or multiple acces channel too)
NHRP is a specific ARP (not routing) mechanism that avoids extra IP hops, its resolution is based on existing routing tables

## Slide 67
NHRP resolution request is passed along NHSs until the request can be answered
Receiving the NHRP reply, the host knows the destination’s ATM address and can thus establish a direct (‘cut-through’) ATM connection
Even within a networks with NHRP capabilities the hosts or routers still have the freedom to decide if the ‘cut-through’ or the routed hop-by-hop connection is used (local decision based on expenses, latency, QoS, etc. requirements)
IPA host
IPB host
SVC
ATMB
NHRP request
HNSA
HNSB
HNSC
LISA
LISB
LISC
‘cut-through’ connection
NHRP reply
NHRP reply

## Slide 68
ATM Local Area Networks
Introduction
LAN Emulation
Multiprotocol over ATM

## Slide 69
Next generation LAN requirements:
Real-time information transfer (ATM-short cells, ok)
Scalable throughput (ATM cells rate, ok)
High transfer capability (ATM up to 620Mbps, ok)
Easily internetworking between LAN and WAN (ATM is a public network standard too, ok)
Standard based solution (ATM is standardised, ok)
ATM Local Area Networks

## Slide 70
ATM LAN solutions:
LAN emulation (LANE) LANE allows ATM to be gradually introduced into existing traditional LANs (it allows coexistence and interoperability among LAN and ATM stations)
Multiprotocol over ATM (MPOA) Based on LANE, MPOA provides end-to-end ‘cut-through’ connections at the network layer (OSI Layer 3)

## Slide 71
ATM Local Area Network Emulation (LANE)
Specified by the ATM Forum (1995, LANEv2: 1997)
It gives a migration path from traditional to pure ATM-based LANs
Several LANs maybe emulated on a single physical ATM network
The main differences needed to be handled by LANE for interoperability of ATM and legacy LAN are:
ATM: connection-oriented communication with local connection identifiers (VPI/VCI)
Legacy LAN: connectionless communication with global addressing (MAC)

## Slide 72
LANE functions can resides in edge devices such as LAN switches, bridges, routers, in legacy LAN to ATM conversion equipment or in native ATM hosts
ATM host
Bridge
LAN
ATM
LAN
Bridge

## Slide 73
LANE is used instead of the MAC (Media Access Control) layer (instead of shared medium ‘broadcast end filter’ transfer technique the point-to-point ATM connections are established between endpoints)
LANE provides the same service primitives to the higher layer as the ‘standardised’ MAC device drivers like the network driver interface specification (NDIS), or open data link interface (ODI) - achieving transparency for all higher layer LAN protocols (e.g. IP, IPX)
Phy
ATM
AAL 5
LANE
Higher
layers
IP/IPX
Phy
MAC
Higher
layers
IP/IPX
Phy
MAC
Phy
ATM
AAL 5
LANE
Phy
ATM
Phy
ATM
ATM Switch
MAC Bridging Edge Device
ATM LANE Station
LAN Station

## Slide 74
ATM LANE basic building blocks
End-systems of a single emulated LAN (ELAN)
Communicating each other via LUNI (LAN emulation user network interface)
LEC handles the data forwarding/reception, address resolution (ATM/MAC) and control functions
Several LEC may exist in those devices simultaneously if they are connected to several ELANs
LEC is a legacy LAN to ATM conversion equipment
Legacy LANs may contain more than one devices, so its LEC represents more MAC addresses (all the MAC addresses of the LAN) and a single ATM address - it is also called Proxi LEC
LAN Emulation Clients (LEC)
LAN Emulation Server (LES)
For each ELAN one LES exists
LES provides the necessary control function, it registers and resolves the MAC and ATM addresses

## Slide 75
Several LANs maybe emulated on a single physical ATM network
LECS has the responsibility of assigning LEC to a particular ELAN
This is done during the initial configuration by transmitting the ATM address of the LES to the LEC
Furthermore, it exchanges information on the own ATM addresses of the LEC, LAN type and maximum allowed frame size (MTU) with the LECs (LECS must contain all these information for all LEC of all ELANs - usually LECS needs to be manually configured by the network operator)
LECs are locating their LECS by:
  well-known permanent pre-configured VCC (VPI=0, VCI=17) (used only for finding LECS)
  obtaining LECS address from its ATM switch via the ILMI management procedure
  using well-known LECS ATM address (different addressing can cause problems)
After finding its LECS, the LEC establishes a Configuration Direct VCC to the LECS
LAN Emulation Configuration Server (LECS)

## Slide 76
Broadcast and Unknown Server (BUS)
Used for ‘flooding’ unknown destination address traffic and multicast/broadcast traffic to all LECs within an ELAN
Each LEC is associated with a single BUS, whose unique ATM address can be obtained from the LES
In additional, BUS can be used for data transfer between LECs as long as no direct point-to-point VCC could be established (for reducing delays of LE-ARP and connection establishment)
Location of the servers
All the server functions can be physically distributed or co-located
e.g. BUS and LES are ideally co-located for sharing a common database, possibly resulting an optimised BUS forwarding policy

## Slide 77
Joining an ELAN and registration
Getting all the configuration information from the LECS, LEC is able to establish a connection to its LES (Control Direct VCC)
LEC registers its addresses (one or more MAC and one ATM address) at the LES
LEC issuing LAN Emulation Address Resolution Protocol (LE-ARP) messages to LES for obtaining any unknown ATM addresses
If the LES does not find the requested address in its cached address table, it forwards the LE-ARP request to all attached LECs, through the point-to-multipoint Control Distribute VCC
The first ATM address the LEC try to obtain is the ATM address of the BUS (this is done by issuing a LE-ARP for the all-1s MAC broadcast address)
Having the ATM address of the BUS, LEC establishes a point-to-point Multicast Send VCC to the BUS and the BUS in turn adds the LEC as a leaf to the point-to-multipoint Multicast Forward VCC
LES normally knows all the addresses of its ATM hosts, but it may not know all the MAC addresses associated to the ATM addresses (e.g. a LAN bridge with many MAC hosts on the LAN side)

## Slide 78
The data transfer phase
Data is transferred in two possible way:
  for broadcast or multicast traffic the LEC transmits the packets to the BUS for further distribution
  for unicast traffic the LEC uses a Data Direct VCC (SVC)
In case of unicast traffic the LEC may find an already existing Data Direct VCC or at least it knows the destination ATM address - this case it can directly establish a VCC
If the destination ATM address is not known, the LEC is issuing a LE-ARP request message to the LES for obtaining the unknown ATM address. The LES may either know the requested address or forward the LE-ARP request to all attached LECs via the Control Distribute VCC. The LEC that knows the correct address mapping will answer via the Control Direct VCC back to the LES. Now the LES may forward this answer either to the requesting LEC only, or all the LECs.
During the waiting period until the LE-ARP answer is received the sending LEC could store (or discard) the packets or send them to the BUS which will flood all the LES. As soon the destination ATM address arrives, (after flushing the broadcasting) the LEC could establish a Data Direct connection.

## Slide 79
LEC within an ATM host
ATM
LAN
Bridge
LEC within a LAN bridge
LECS
a
a
LECS
b
b
c
BUS
d
d
e
a: Configuration direct VCC
b: Control direct VCC
c: Control distribute VCC
d: Multicast send VCC
e: Multicast forward VCC
f: Data direct VCC
f

## Slide 80
Advantages and disadvantages of LANE
LANE allows network administrator to build Virtual LANs (VLAN). VLAN allows end-systems to be assigned a logical group (logical LAN). Having the same physical ATM network VLANs are built by allocating a LEC to a specific ELAN (LES). Interconnecting ELANs (VLANs) routers needed to be used.
Interconnecting different type of ELANs (e.g. Ethernet - Token Ring) needs router (a LEC can belong only to one type of ELAN and a direct connection between different e.g. ‘Ethernet LEC’ and ‘Token Ring LEC’ is not possible)
Since LANE is a bridging technique, it is susceptible to large amounts of broadcast traffic, which might easily flood the entire network. This may cause congestion even on a high-speed ATM network. The LANE servers, LES and BUS constitute potential bottlenecks as well.
LANE is limited for ‘small’ networks

## Slide 81
ATM Multiprotocol over ATM (MPOA)
Specified by the ATM Forum (1997)
The main goal of the MPOA is giving a service which provides end-to-end ‘cut-through’ connections at the network layer (OSI Layer 3)
Communication over several subnetworks requires routers which are potential bottlenecks. MPOA allows optimal, direct end-to-end communication over several subnetworks (having the same physical ATM network) without crossing any router.
Although MPOA allows any existing network layer protocol to be used, such as IP, IPX, AppleTalk, DECnet, the ATM Forum focused its initial work on supporting TCP/IP networks.

## Slide 82
MPOA basic principles
MPOA uses LLC/SNAP encapsulation and the ‘overlay’ model, where layer 3 addresses are assigned independently of ATM addresses and where layer 3 routing protocols such as OSPF run separately from ATM routing such as PNNI
For resolving layer 3 to ATM addresses MPOA makes use of the NHRP and its NHS
MPOA reduces overhead and broadcast traffic while supporting larger MTU sizes and making full use of ATM’s QoS capabilities (direct end-to-end ATM connection)
MPOA builds upon a distributed router or virtual router model
The two main tasks of a traditional router are the route processing and the data forwarding. MPOA makes an attempt to distribute these functions on discrete devices: MPOA Clients (MPCs) for switching and forwarding, and MPOA Servers (MPSs) for building routing tables (route processing)
MPCs connecting legacy LANs to ATM network are also called edge devices

## Slide 83
MPOA Client (MPC)
MPC communicates with its MPS via definde protocols
MPCs builds the endpoints of a communication association
They may reside in MPOA capable ATM hosts or in edge devices (devices connecting legacy LAN equipment with an ATM network)
MPC can be considered to be an intelligent multilayer switch, since it evaluates either the destination MAC address (in case of staying in the same ELAN) or the destination network layer address to forward data frames.
MPOA Server (MPS)
MPS is a route server comprising the set of functions to build routing tables and to be able to answer address queries
MPS maintains MAC layer, network layer, and ATM layer address mappings and runs a routing protocol such as OSPF (Open Shortest Path First) or RIP (Routing Information Protocol) to communicate with traditional routers
MPS can be considered to be an enhanced NHS
MPS can be realised in a dedicated device or be integrated into existing router

## Slide 84
Principles of data flow
As long as a data flow stays within a single ELAN, communication is based on LANE principles
In case of inter-ELAN communication two possibilities exists to forward data: either on hop-by-hop basis form router to router, or using a short-cut connection which directly connects two MPCs
In inter-LAN communication by default MPCs sending data packets to the default MPS (via LANE), which acts as a ‘traditional’ router
As soon as MPS detects a ‘flow’ of packets (several subsequent packets with the same layer 3 address within a given time interval) it attempts to establish a cut-through connection
If the destination ATM address for this layer 3 address is not known, an MPOA resolution request needs to be issued first (it resolved according to the principles of the NHRP)
Having the destination ATM address for this layer 3 address, the source MPC establishes a cut-through VCC connection to the destination MPC
MPCs and MPSs automatically discover each other using a modified LANE ARP protocol

## Slide 85
MPOA data flow
MPC source host
SVC
ATMC
Router/ MPSA-B
ELANA
ELANB
ELANC
‘cut-through’ connection
LAN
Bridge
MPC Edge Device
ATM
Router/ MPSB-C
ATMA
Destination host
Routed default path
Cut-through connection

## Slide 86
Ethernet (MTU: 1500 Byte) = 32 cells
FDDI (MTU: 4470 Byte) = 96 cells
IP over ATM (MTU: 9180 Byte) = 192 cells
Loosing even a single cell may destroy the whole packet
A single bit failure causes 32 cells loss (Ethernet)
This may cause congestion even on a high-speed ATM network
Legacy LAN packet over ATM
X
Sensitivity for cell losses in Legacy LAN packet over ATM techniques

## Slide 87
ATM Forum was founded in 1991
Founders: Cisco Systems, NET, Nortel, Sprint
Nowadays ATMF has more than 700 members
ATMF Working Groups: Signaling, UNI, PNNI, LANE, MPOA
http://www.atmforum.com
ATM Forum:

## Slide 88
http://www.cisco.com
http://www.atmforum.com
e-mail info@atmforum.com
http://cella-relay.indiana.edu
http://www.atmreport.com
http://www.atm-user.com
ATM References:
Books:
R. Händel, M.N.Hube, S. Schröder: ATM Networks (Addison-Wesley, 1998)
D. Ginsburg: ATM solutions for enterprise internetworking (Addison-Wesley, 1996)
WWW sites: